## Slide 1: Crowd sourcing techniques and applications for ITS Limitations and possibilities
Dionisis Kehagias
Senior Researcher at Information Technologies Institute /
Centre for Research and Technology Hellas (CERTH/ITI)
1st MOVESMART Workshop, 15 October 2015, Bilbao

## Slide 2: Crowd Sourcing Scenarios
The system incentivise users so that they provide consent on the collection of location data anonymously.
As the users are moving, spatiotemporal data (position, speed) are collected passively, through the traveller monitoring cloud service and stored to the UTKB, on their consent.
User real-time traffic data are used by:
  The user feedback assessment operation
  Traffic prediction module for:
    Updating historical database
    Performing real time predictions
On-route working scenario

## Slide 3: Crowd Sourcing Scenarios
A random user sends a report (e.g. “high congestion on Elm Street”).
The CSM retrieves user credibility by looking up the user feedback database (UFDB).
If the user is credible, CSM sends out the reported information to all users that are located around the reporting user. It requests users to evaluate the reported information at a later stage.
Otherwise, the system sends a feedback request message about the incoming report.
It collects user feedback to assess the credibility of the reporting user.
Emergency report working scenario

## Slide 4: Crowd Sourcing Scenarios
A random user is asked to evaluate the provided alerts
  True or False
Based on the user’s feedback
  The CSM collects user feedback to assess the credibility of the reporting user providers.
Post-route report scenario

## Slide 5: Crowd Sourcing Framework: Structure and Functionalities
Crowd sourcing module architecture

## Slide 6: Users Ranking Mechanism and Credibility Estimation: the Movesmart approach
Ranking mechanism
Criteria
  Semantic Similarity (Rs): represents the similarity of the information provided by a user with respect to other information submitted in the same time window by nearby located users.
  User’s Credibility (Rr): each user has a dynamic score that represents their Degree of Reliability, based also on other user’s feedback.
  Call Frequency (Rf): each user has a dynamic score that represents the reporting frequency of the user. A user that reports rarely gets a low score as opposed to a frequent reporter.
  Relevance Feedback (Rd): a score of how the other users evaluate the reported information.
  Response Time (Rt): A score that illustrates if the user responded on time.
Overall Score

## Slide 7: Rs - Semantic similarity
Each report is characterized by a tag t that describes the type of the event e.g. Incident, Weather, Traffic Jam.
uc is the current user that makes a report for an event at a specific place in a specific time window
tc the tag of the event.
u1, u2, …, uN other nearby located users that report events at the same time window with tags t1, t2, …, tN.
The tag tc is compared with all the tags t1, t2, …, tN and the mean value of the results gives the factor Rs. Hence the factor Rs is given by:

## Slide 8: Rr – User’s credibility
p(e1), p(e2), … , p(eN) are calculated using a probabilistic framework
The factor Rr represents a reliability degree of a user. If a user u has submitted N event reports e1, e2, … , eN until now, with probabilities p(e1), p(e2), … , p(eN) of being true, then the Rr factor is calculated by the following equation:

## Slide 9: Rf – Call frequency
The factor Rf refers to the frequency with which a user submits reports. If N is the total number of reports that have been submitted to the system until now, and M is the number of reports that the user u have submitted the Rf is given by:

## Slide 10: Rd – Relevance Feedback
The Rd factor represents the relevance feedback from users about a specific alert. Users can either confirm or reject every event report that is submitted to the system.
For a user alert:
  C confirmations
  R rejections from other users

## Slide 11: Rt – Response Time

## Slide 12: Credibility estimation
What if the user is not in an optimal position to send an alert?
What if not a sufficient number of users submit feedback?
How to deal with malicious users?
How to deal with a reliable user who turned to be malicious?
How often should feedback be updated?
Crowd sourcing challenges
In order to deal with those challenges we need a feedback resolution mechanism: e.g. majority vote

## Slide 13: Crowd sourcing collected data
On-route data (collected by the user’s device as the user is moving on user’s consent):
  user location
  user speed
Post-route data:
  Relevance Feedback: 1-5 stars rating
Emergency data:
  Weather info (e.g. sudden change of weather conditions)
  Incidents (e.g., accidents, demonstrations, etc.)
  Public Transport info (e.g. bus delays)
  Traffic info (e.g. report of high congestion).

## Slide 14: Credibility estimation
Conceptual Idea
Decreasing Creditability
Location of the declared event
Far
Average
Distance
Average
Distance
Close
Unreliable Users
Reliable Users
Definition: We define the probability of an event e to be true as
Assumption 1: Specific contextual conditions, occurring at the time instant an event is declared, are expected to evaluate the user’s perception capacity (intended or not).
Assumption 2: The contextual parameters are considered statistically independent (i.e. 1D distributions), unless declared/proven otherwise (i.e. joint probabilities)

## Slide 15: Credibility Estimation - 1D Distributions
Decreasing
Credibility
d1: Normalized
average speed
Average speed of
the reporting vehicle
d2: Distance
from incident
Location of the
declared event
Decreasing Credibility
denotes the probability of a distant user is reporting a false event
denotes the probability of a fast moving vehicle/user is reporting a false event

## Slide 16: Reliability Assessment Framework
Let r be an incoming user’s traffic report
Define event:
Assumption: The probability of r being true depends on reporter’s traits (Xsi) e.g. the speed of the reporter at the time of the report submission
Conditional probability of the report being true:
At this point 3 reporter’s traits are used:
  Xs1: The distance of the reporter from the location of the reported event
  Xs2: The speed of the reporter at the time of the report submission
  Xs3: The number of negative evaluations of the report from other users

## Slide 17: Probability Calculation Model
where
Traffic incident report probability of being true
Based on Bayes theorem:

## Slide 18: Simulation Framework
Report
  The report send from the user has the following format:
  ReportID, Timestamp, Longitude, Latitude
Reporter
  The reporter traffic information recorded at time of the report have the following format:
  UserID, Timestamp, Longitude, Latitude, Speed
User traffic records
  The users traffic records have the following format:
  UserID, Timestamp, Longitude, Latitude, Speed
Data derived through simulation process

## Slide 19: Results after Running the Simulation
Probability of being true vs. user speed

## Slide 20: Results after Running the Simulation
Probability of being true vs. user distance from the event

## Slide 21: Rule Generation

## Slide 22: Traffic Prediction
The Goal: Use traffic prediction for better routing
  Avoid major delays due to traffic jams
  Consume less energy / produce less pollution
Objective of Classic Traffic Prediction Techniques:
  Predict travel time (time required to traverse the link) based on historical and real time data drawn from GPS devices, etc.
Objective of CS-based Traffic Prediction
  Implement efficient algorithms for predicting traffic under atypical conditions and test with historical/real traffic data

## Slide 23: Taxonomy of Classic Traffic Prediction Techniques
Classic Traffic Prediction Techniques
Parametric
Naive
Historic average
AR/MA/ARMA/ARIMA
STARIMA
Lag-based STARIMA
k-Nearest Neighbor (kNN)
Artificial Neural Networks (ANN)
Support Vector Regression (SVR)
Hybrid
Non-Parametric

## Slide 24: Use of Crowd Sourcing for Traffic Prediction
Main idea: Identify the traffic pattern of specific type of atypical conditions (e.g. sports events) and dissociate it from the “typical” one.
Weekdays
Weekends
Typical
Atypical
Typical
Atypical
Neither typical nor atypical (e.g. “close to atypical”)

## Slide 25: Traffic Predictor Under Atypical Conditions Algorithm (TPUAC)
  Step 1: Separate weekdays and weekends
  Step 2: Determine optimal number of clusters for each set
    Elbow method
    Silhouette
  Step 3: K-means clustering for identifying typical and atypical traffic patterns as well as “close to typical”, “close to atypical”, etc. ones
  Step 4: Implement a different set of prediction models for each cluster
    K-Nearest Neighbor (kNN) or Support Vector Regression (SVR)
    1 model per time interval

## Slide 26: Future/Ongoing Work
Test functionality using more real traffic data from the cities of
  Vitoria-Gasteiz
  Pula-Pola
… including the acquisition of historical data for training Traffic Prediction algorithm

## Slide 27: Potential Extensions
Acquire real data (both traffic and incident reports) from pilot cities to test the TPUAC model. Not sufficient data exist yet.
Implement a new algorithm for predicting traffic under atypical conditions that will exploit information from social media (e.g. Twitter)

## Slide 28: Q & A